## Slide 1: Fast pressure distribution prediction of airfoils using deep learning
Presentation : Hyejin Kim
Xinyu Hui1, Junqiang Bai1, Hui Wang1, and Yang Zhang2,3
1School of Aeronautics, Northwestern Polytechnical University
2State Key Laboratory for Strength and Vibration of Mechanical Structures, School of Aerospace Engineering, Xi'an Jiaotong University
3National Key Laboratory of Science and Technology on Aerodynamic Design and Research,
Aerospace Science and Technology, Vol. 105, October 2020

## Slide 2: Introduction
Time consuming due to the inherent complexity of fluid dynamics
  Complexity of Simulations
    Navier-Stokes equations
  Spatial and Temporal Resolution
    To model fluid flow accurately, a high spatial and temporal resolution, especially for turbulent flows or flows with small-scale features are needed
  Meshing
    The quality and resolution of the mesh significantly impact simulation accuracy, and generating a suitable mesh can be a non-trivial process
Computational fluid dynamics (CFD)
Construct surrogate model by introducing deep learning

## Slide 3: Machine learning method
1. Data generation
  Airfoil library (Using Latin Hypercube Sampling (LHS), Free-Form Deformation (FFD))
    FFD is a powerful tool in the geometric design of 2D and 3D objects
    Each control points can move perpendicular in the range of [−0.02, 0.02]
Entire framework
Airfoil geometry
Control points
Dataset airfoil library
Sampling by LHS
1,500 airfoils are generated
Upper surface
Lower surface
Pressure coefficient (Cp)
Validation CFD solver
flow condition of free-stream
Mach number :
Reynolds number :
Angle of attack :
Mesh
RAE2822

## Slide 4: Machine learning method
1. Data generation
  Representation of airfoil geometry by SDF
    The airfoils are converted 32by32 cartesian grid by using Signed distance function (SDF)
Entire framework
Airfoil geometry
Control points
Dataset airfoil library
Sampling by LHS
1,500 airfoils are generated
Upper surface
Lower surface
SDF of base airfoil RAE2822 in a 32 ×32Cartesian grid
Like 2D image!
Airfoil
Signed distance function (SDF)
Signed distance function :
Airfoil boundary :
measures the distance from to its nearest point
determines whether the point is in-side or outside the airfoil
: Inside
: Outside
Notes: Here, the points outside the airfoil have positive values, and de-crease as the points approaching to the boundary of the geometry where the values are zeroes, and they become negative once inside the airfoil.
To generate the SDF for objects, the background mesh is an evenly distributed Cartesian grid.

## Slide 5: Machine learning method
1. Data generation
  Datasets consist of 2D airfoil image and corresponding Cp
Entire framework
The SDF representation of base airfoil RAE2822 in a 32 ×32Cartesian grid
Like 2D image!
Airfoil
Pressure coefficient (Cp)
Datasets
(X, Cp)
Split()
Training data
Testing data
Mesh
2D airfoil images for each airfoil shape
Corresponding pressure coefficient

## Slide 6: Machine learning method
2. Training phase
  Convolutional neural network
    Convolution filter(kernel)
    Optimizing Weight and biases
Entire framework
< Input > Airfoil image
< Output > Airfoil pressure coefficient
Extract local features/patterns
Convolution filter
weight
bias
Activation function
Notes: During the convolution process, each fil-ter will slide across the input’s width and height, giving us the responses at every spatial position.
Through the accumulation of each layer, this network will learn the entire patterns

## Slide 7: Result and discussion
Hyperparameter
  These networks are investigated by varying the number of convolutional layers
  Training under Adam optimizer and MSE loss function
Parameters setting
Network hyperparameter
Fully connected neural network
Convolution neural network
Network parameter optimization
is the learning rate
batch size is 50
Notes: The number of layers, number of nodes in each layer, kernel size, and choice of activation functions are often referred to as hyperparameters which are usually selected before training.
Furthermore, all the hyperparameters, such as learning rate, batch size, and any parameters that need to be decided before training, will be consistent between CNN and FNN.

## Slide 8: Result and discussion
Convergence history of the designed CNN architectures of upper and lower surface in training and validation datasets.
  CNN-C5 architecture is considered as the base model for further study because of its steady performances
Pressure coefficient prediction based on CNN
Upper surface
Lower surface
CNN-C5
Convergence history of the designed CNN architectures
Test accuracy for upper and lower surface
Predicted Cp of random sampled airfoils
CNN-C5
Notes: At the leading edge, CNN performs worse because of the variation in the leading edge along Ycoordinate. Around the shock wave zone, CNN performs great, which proves that our model can capture the nonlinear features that play an important role in fluid mechanics.
As can be seen, these four pressure forms show different features from the original airfoil RAE2822. Either a double shock structure or strong shock waves are detected for these airfoils.
At the leading edge, CNN performs worse because of the variation in the leading edge along Y coordinate.
Around the shock wave zone, CNN performs great, which proves that our model can capture the nonlinear features that play an important role in fluid mechanics.

## Slide 9: Result and discussion
Retrain and test the CNN-C5 model on new base airfoil model : S809
  New dataset is employed to prove the robustness of CNN-C5 model
Pressure coefficient prediction based on CNN
Predicted pressure coefficient of S809 airfoil
S809 airfoil
Upper surface
Lower surface
Convergence history of the CNN-C5
flow condition of free-stream
Reynolds number :
Angle of attack :
Notes: S809, whose aerodynamic characteristics are representative of wind-turbine airfoil

## Slide 10: Result and discussion
The performance comparison between CNN and FNN
  Training and test loss convergence history
  Training time
Performance comparison between CNN and FNN
Convergence history of CNNs and FNNs in training and validation datasets of upper surface
Comparison of time requirements.
Notes: S809, whose aerodynamic characteristics are representative of wind-turbine airfoil
At last, the summary of the computational time of the model training and prediction are shown in Table3, along with the time required for CFD simulations. CNN-C5 training saves more than half of the time compared to FNN-L5. Because the number of pa-rameters of CNN is remarkably reduced by the convolutional func-tions, where FNN-L5 must handle 102400 parameters when the information flows through the last layer, only 14400 parameters are considered by CNN-C5. CNN keeps accuracy and efficiency at the same time.

## Slide 11: Result and discussion
The performance comparison between CNN and FNN
  It is apparent that all three FNNs fail to capture the aerodynamic features
Performance comparison between CNN and FNN
Predicted pressure coefficient predicted by CNN and FNN
discrepancy
Notes: It is apparent that all three FNNs fail to capture the aerodynamic features, especially for FNN-L7, its model collapses cause the pressure shown in four variants are precisely the same.

## Slide 12: Conclusion
Methodology to predict the pressure distribution (Cp) over an airfoil using deep learning (CNN) is proposed.
To effective deal with data, SDF method is introduced to convert airfoils into image data
Comparing between conventional FNN and CNN, it is observed that CNN has superior performance dealing with image data.
Further analysis of CNN, the test results has good agreement with original data.
Conclusion
Notes: S809, whose aerodynamic characteristics are representative of wind-turbine airfoil